## Slide 1: 2 element receive array for 160m at W6AYC
Motivation
  K9AY array (7 dB RDF) always superior to TX antenna (5 dB RDF) but better performance desired
Constraints
  Limited flat yard space available
  4 direction instantaneous switching desired
Options considered:
  Shared Apex array (8 dB RDF)
  2 phased verticals (9 dB RDF)
  Waller Flag (12 dB RDF)

## Slide 2: Tradeoffs
Shared apex array
  Pro- Small footprint, ground independent
  Con- Minimal improvement over K9AY, doesn’t fit that well in available space
Two verticals spaced 1/8 wavelength
  Pro- at least 2 dB better than K9AY, instantaneous direction switching, four-direction array fits in my yard, high output level (no preamp required, common mode not a big problem)
  Con- only 2 dB RDF improvement, have to run feedlines to each vertical and design a phasing box
Waller flag
  Pro- excellent directivity
  Con- physical rotation required, low output level requires special attention to preamps and common mode noise
2 element vertical array chosen for development.
Waller flag might be an extremely interesting educational experience in the future.

## Slide 3: Array of 2 element verticals
Design
  Array
  Vertical elements
  Phasing versus antenna pattern
  Crossfire phasing
Construction
Results
Future work
Design was based on material from ON4UN’s Low Band Dxing, W8JI’s website and the YCCC 9 circle array manual (W1FV).

## Slide 4: Delay is added in Antenna 2 feedline so that signals from left arrive at the combiner 180 degrees out of phase
Desired signal direction
Combiner
Delay
Receiver
Antenna separation
Antenna 2
Antenna 1
-Delay is in feedline of antenna in the direction of receiving
-Close spaced arrays have lower output and are more critical for
phasing
- Example: Antenna separation of 45 degrees and phase delay
of 135 degrees gives 180 degrees difference at the combiner
for signals from the left, causing cancellation (at 0 degree elevation)
- We usually move the nulls up in elevation by increasing delay

## Slide 5: Layout of array at W6AYC
NW vertical
NE vertical
67 feet
60 feet
Corner vertical
Array of 3 verticals, two used at a time (NW/SE and NE/SW)

## Slide 6: Vertical elements
Passive elements with umbrella loading wires ala W8JI chosen for simplicity and robustness
  24 foot verticals with three 20 foot umbrella loading wires
  Larger elements minimize sensitivity to surrounding objects
  Large electrical size maximizes bandwidth
  Umbrella wires guy the verticals
  Earlier work showed short verticals to be very sensitive to surroundings. This is sometimes attributed to capacitance to surrounding objects. A better explanation is that the small capture area is overwhelmed by reradiation from local objects. Short verticals with high impedance amplifiers are great for clear pastures.

## Slide 7: Simulation of vertical 24 foot element with three 20 foot umbrella wires
Input impedance is 0.8 –j 530 at 1.8 MHz.
Imaginary part drops to -160 Ohms at 80m.
Asymmetry of umbrella wires has little effect

## Slide 8: Vertical elements will be matched to 75 Ohm RG-6
Series inductor used to cancel –j530 Ohms plus a series resistor to match to 75 Ohms
Resistive matching and 75 Ohm cable maximizes bandwidth
  Output signal levels are high so resistive matching is tolerable
  Mismatch causes amplitude and phase errors. ON4UN’s analysis indicates maximum voltage and phase errors of about 5% for VSWR=1.1 (26 dB return loss) and 10% for VSWR= 1.2 (21 dB return loss).
  Voltage errors degrade null depth. Phase errors move the nulls around.

## Slide 9: A DPDT direction relay places the delay in either feedline
Combiner
Delay
Receiver
Antenna separation (67 or 60 feet)
Antenna 2
Antenna 1
Feedline length 69 feet
Feedline length 69 feet

## Slide 10: Optimum delay is 145 degrees- good for 67 and 60 foot spacing
160m, 67 foot spacing
160m, 60 foot spacing
135 degrees
155 degrees
145 degrees
135 degrees
155 degrees
145 degrees

## Slide 11: Little change in nulls between 60 and 67 feet spacing
160m, 67 foot spacing
135 degrees
155 degrees
145 degrees
135 degrees
155 degrees
145 degrees
160m, 60 foot spacing

## Slide 12: Pattern is still good on 80m
135 degrees
155 degrees
145 degrees
90 degrees
130 degrees
110 degrees
160m, Directivity= 9.4 dB
80m, Directivity= 8.7 dB

## Slide 13: RDF gets better with increasing phase Front beam narrows but rear lobes increase

## Slide 14: Antenna control
An array relay will select either the NW/SE or NE/SW array
A second relay controls the direction of the selected array
Delay is implemented by “crossfire phasing”
  Popularized by W8JI
  Large bandwidth allows a single array to work on 2 and sorta 3 bands
  Uses minimal length of coaxial delay line

## Slide 15: Cross-fire phasing compensates for spacing between antennas allowing multiband operation
180 degree
transformer
Delay line
Output
Input
Output= 180 degrees – delay
For example: 160m antenna spaced 45 degrees with crossfire phasing and a 35 degree delay line is usable
on 80m and somewhat on 40m.
Freq Ant separation Delay line Cross-fire delay Total delay
1.8 45 35 145 190
3.6 90 70 110 200
7.2 180 140 40 220
All numbers are degrees.

## Slide 16: Construction- Vertical elements
24 foot verticals constructed of telescoping aluminum
NW and center attached to fence posts with hose clamps
NE vertical mounted on aluminum stake
Three 20 foot umbrella wires for guying
Ground system consists of fence plus three 50 foot radials
Feedlines are choked by W1FV common mode choke from YCCC kit

## Slide 17: NW vert measured input impedance, -j477 Ohms

## Slide 18: Center vert measured input impedance, -j426 Ohms

## Slide 19: NE vert measured input impedance, -j436 Ohms

## Slide 20: Inductor using powdered iron cores 41T, T106-1, Q=50
Molded inductors could be used but may be susceptible to ESD damage.

## Slide 21: Matching network

## Slide 22: Return loss of verticals is better than 10 dB (VSWR=2) over 150 kHz
NW
Corner
NE
5 dB
15 dB
25 dB
35 dB
10 dB
20 dB
30 dB
Frequency could be lowered by
bunching inductor turns
0 dB
Rtn
Loss (dB)

## Slide 23: Phase controller box
RX Output
Corner Vertical
NW Vertical
NE Vertical
Wires
Yellow- ant select
Gray- phase select
Black- ground

## Slide 24: Controller is built on perf board
Dead bug relays
2:1 Xfmr
Power splitter
Phase inverter

## Slide 25: Phase box schematic
Output to RX
Corner
Delay line connection
3 Ohm, 0.3 dB attn
(75 Ohm)
(35 Ohm)
150 Ohm
Impedance Xfmr
7T/5T
Power Splitter
7T/7T
Phase Inverter
6T/6T
All xfmrs use binocular cores
Fair-Rite 2873000202, Type 73 material
Relays are Panasonic
DS2Y-SM-DC12V
NW
NE
(75 Ohm)
(75 Ohm)
Phase Relay
Array Relay
(circuit impedance)
NC
NC

## Slide 26: Hi-tech direction controller using two SPDT switches

## Slide 27: 44 foot RG-6 delay line= 35.5 degrees

## Slide 28: Phase box gives 143 degrees delay 0.1 dB greater loss in delay side

## Slide 29: EU Return Loss- In shack measurement is good for verifying both dipoles are being combined

## Slide 30: SE Rtn Loss

## Slide 31: JA Rtn Loss

## Slide 32: SE Rtn Loss

## Slide 33: Results and thoughts
Front-to-back varies from impressive (15 to 20 dB) to nominal (5 dB) with fading
  Much better than the typical 6 to 12 dB with K9AY
Evaluation is subjective and difficult
Front-to-back isn’t really an issue for us on the west coast
  RDF is most important but hardest to demonstrate
  Good front-to-back is reassuring
My experience with RX antennas indicates the 2 to 4 dB expected SNR improvement over the TX antenna is difficult to demonstrate most of the time
  When noise pops up directivity can be a phenomenal help

## Slide 34: Future work
Push button controller for direction control
Expand coverage to 80m
  Dual band matching network may limit bandwidth
  Diplexer driving parallel matching networks may be better option

## Slide 35: Appendix

## Slide 36: YCCC Choke (W1FV) is excellent for 160 and 80m

## Slide 37: Calibration on corner antenna, NC end leads by 143 degrees Points SE in NC phase

## Slide 38: Output of phase control box return loss

## Slide 39: Leg antenna of phase control box return loss

## Slide 40: Corner antenna of phase control box return loss

## Slide 41: 50 dB isolation to unswitched antenna