## Slide 1: HF Receiving Loops for Direction Finding (Noise Hunting)
Notes on small loops including shielded loops
160 thru 40m tunable multiturn loop
20m loop
6m loop

## Slide 2: Small receiving loops ARRL Antenna book gives excellent explanation of directivity and polarization
Circumference < 0.085 wavelength
Length of sides
1.8 MHz 11.6 ft
3.5 MHz 6.0 ft
7 MHz 3.0 ft
14 MHz 1.5 ft
21 MHz 1.0 ft
28 MHz 9 inches
50 MHz 5 inches

## Slide 3: Shielded Loop only Helps with Symmetry
Shield is receiving antenna
Inner conductor is part of feed system
Outer loop shield which receives signal is not “broken” by feed
  Aides symmetry
  No feedline “pickup”
I don’t agree with ARRL Antenna book statements about asymmetric stray capacitance
30 to 40 dB nulls possible for shielded loops
15 to 20dB nulls more typical for “regular” loops (good enough for DF)

## Slide 4
160- 40m direction finding
loop for locating RFI

## Slide 5: Design
Determine capacitance range of air variable on hand
Measure inductance of single turn of hand help loop
Determine number of turns required to resonate with available capacitor at 160m
Match with step down transform using Type 61 ferrite core ala N6RK

## Slide 6: Max cap- 900 pF, -j97 @1.8 MHz Need loop inductance greater than j100 Ohms

## Slide 7: Min cap- 32 pF, -j700@ 7 MHz

## Slide 8: Measuring 1 turn loop

## Slide 9: 1T 22 inch sides- 3uH, j34 Ohms @ 1.8 MHz Need 3 turns for j100 Ohms

## Slide 10: 3T required to resonate with air variable

## Slide 11: S21 (parallel resonance) loop tuned to 1.8 MHz

## Slide 12: S21 min cap, doesn’t quite reach 40m

## Slide 13: Matching transformer secondary >125 uH, SRF 13 MHz
32T, Type 61 core

## Slide 14: Matching at 1.8 MHz, single turn secondary Could use more turns on primary but this will give good enough efficiency for RX

## Slide 15: Matching at 3.5 MHz

## Slide 16: Matching at 6.6 MHz (max tuning frequency)

## Slide 17: Conclusions
DF loop gives nulls of >15 dB from 160 to 40 meters
Bandwidth is narrow (tuning is sharp) at 160m
Greater gain at 40m overcomes mismatch loss. Lower Q makes tuning uncritical

## Slide 18: 20m DF loop

## Slide 19: 22 inch sides: 2 uH, j170 at 14 MHz

## Slide 20: Resonated with 68 pF

## Slide 21: 15T primary on FT-82A-61 core 3500 Ohm reactance, SRF= 25 MHz

## Slide 22: 1T secondary

## Slide 23: Results
>15 dB nulls

## Slide 24: 50 MHz Loop

## Slide 25: Match using parallel capacitor followed by series capacitor High ratio transformers are difficult at 50 MHz

## Slide 26: 6 inch sides: j180 Ohms at 50 MHz

## Slide 27: Matching with 10 pF parallel, 5 pF series ceramic caps

## Slide 28: Results
Matching worked well
Sensitive to common mode on coax shield
Poor directivity
  Minimizing area of matching network didn’t help
Added two additional Type 31 clamp on ferrites
  15 dB nulls, similar to other loops