## Slide 1: High efficiency vertical for 7, 14 and 21 MHz
2nd antenna for SO2R operation
Vertical polarization to increase isolation to primary (beam) antennas
Omni pattern for quick QSO’s without rotating beam
Radiation angles below 15-20 degrees needed (from statistics in HAFTA)
Rather than use a 15m trap, operate as a quasi 5/8 wavelength improving gain by several dB

## Slide 2: 34 foot vertical at 7 and 21 MHz 21 MHz has less ground loss
¼ wavelength vertical for 21 MHz (11.5 ft)
-1.4 dBi gain at 15 degrees
34 ft vertical has 1.0 dBi gain at 15 degrees
21 MHz
7 MHz

## Slide 3: 34 foot vertical at 7, 14 and 21 MHz Note increased efficiency at 21 MHz in far right column

## Slide 4: At 21 MHz efficiency of a vertical monopole increases with height from 24 to 34 feet

## Slide 5: Radiation pattern of vertical monopole at 21 MHz l= 24,27,30, 33 and 36 feet
Low angle radiation (15 degrees)peaks
at 2.5 dBi around 30 feet in length and
then decreases rapidly as power shifts
to higher lobes
30 ft
36 ft
33 ft
24 ft
27 ft

## Slide 6: Design
Challenge: Make 15 meter radiation pattern more like a 5/8 wave antenna by lowering physical height of current maximum while maintaining low enough feed-point impedance to match antenna on all three bands with one matching network
Solution: Single 20m trap. Adding top loading below trap lowers height of 15m current peak while lowering feed-point impedance. Top loading is highly efficient for 20m radiator and has minimal effect on 40m.

## Slide 7: 27.5 foot high efficiency vertical for 7, 14 and 21 MHz
7.5 ft
(5.5 ft long)
9.0 ft
27.5 ft
Feedpoint
20m trap
20m top loading stubs
0 ft

## Slide 8: Design methodology and constraints
Recycle tee bar from old Force 12 vertical dipole for first section to loading stubs (7.4 feet long)
Design for 30 to 70 Ohms capacitive reactance at resonance on 20 and 40m. Use hairpin matching of the approximately 30 Ohm real part
Test antenna affixed to a ground stake allowing ease of tuning
  Account for 20 to 30 Ohm ground loss
  Resonances will be unaffected
Install on roof with hairpin and final tune

## Slide 9: 7 and 14 MHz gain is -1.4 dBi, 21 MHz gain is +2.6 dBi at 15 degrees elevation over poor ground
21 MHz
7, 14 MHz

## Slide 10: Simulation details

## Slide 11: Simulation with perfect ground shows trap loss <0.2 dB for Q= 200 inductor

## Slide 12: Simulated result using a 1 uH Hairpin (20m)

## Slide 13: 40 and 15m simulated result with 1 uH Hairpin

## Slide 14: As built
7’ 4” to tee
Tee to coil 20”
Length 27.5’ adjustable to 31’

## Slide 15: Trap adjusted for 13.78 MHz (2.0 uH, 67 pF) Resonance below band minimizes losses

## Slide 16: Tuning rules
Shortening stubs raises 15m impedance and primarily 20m frequency
5.5 to 6 foot optimum stub length
Length= 27 feet, longer lowers 21 MHz real part but becomes inductive

## Slide 17: Antenna mounted to ground stake for initial tuning 68 inch stubs, 15 to 25 Ohm ground loss

## Slide 18: 68 inch stubs- should hairpin match OK with lower ground losses of roof mounting

## Slide 19: Will roof mounting affect low angle lobes? Vertical raised to 15 feet improves 20m slightly while 15m degrades slightly
See K9YC’s study of raising HF verticals
above ground

## Slide 20: Roof mounted antenna Real part is 33 Ohms on 40 and 20m (measured at feed point)

## Slide 21: 1.5 uH Hairpin added

## Slide 22: Return loss measured in shack

## Slide 23: 40m return loss

## Slide 24: 20m return loss

## Slide 25: 15m return loss

## Slide 26: Conclusions
Antenna is easy to match on 40 and 20m
It’s a struggle to get 21 MHz real part less than 100 Ohms
  VSWR=2 is easily handled by radio and amplifier antenna tuners
  Additional loss due to VSWR in 75 feet of RG-8 is about 0.1 dB
On-air performance seems fine
  Typically 1 to 2 S-units down from beam at 60 feet
  Less than 1 S-unit at low angles on 40m (Europe)
  Always better than operating off back or sides of beam

## Slide 27: Appendix
Coil measurements

## Slide 28: Notes on measuring coils with VNA
Three measurement methods using VNA
  S21 method is more accurate for high impedances
  S11 method is better for impedances around 50 Ohms
  Shunt-thru method is better for low impedances
S11 and S22 methods give similar results for inductance measurement
Q measurement is best done with shunt-thru resonator method due to low resistance (ESR)

## Slide 29: Coil measured using S21 method

## Slide 30: Resonated with 67 pF, S21method

## Slide 31: Coil measured using S11 method

## Slide 32: Resonated with 67 pF, S11 method

## Slide 33: Measurement of resonator Q

## Slide 34: Q= 175 (assuming Q of ceramic capacitor is >> than Q of inductor