## Slide 1: Objective: Evaluate XM240 loading coil
Method
  Fabricate test coil with same characteristics as XM240 coil
    Better test measurement accuracy without aluminum tubes
  Measure Q at 7 MHz and SRF
  Add capacitive hat
    Evaluate effect on loading coil (is SRF lower affecting performance?)
XM240 loading coil
  68T
  12 Ga enamel wire
  ¾ inch fiberglass rod
  5.57 inch long

## Slide 2: Brian Beezley’s Coil 4.09 predicts L= 8.6 uH, Q=272

## Slide 3: Test coil fabricated using fiberglass rod from Max Gain Systems
62.5T, 12 Ga Enamel wire
Hand wound coil is not quite as tightly wound as commercial version but should still be representative

## Slide 4: Measurements made using two port VNA Thru (S21) measurement is more accurate for high impedances
L= 9.1 uH, SRF= 45 MHz

## Slide 5: To measure Q, the coil is resonated at 7 MHz with a ceramic capacitor and the insertion loss of the parallel resonant circuit measured Q= center frequency divided by the 3 dB bandwidth
Measured Q= 240
56 pF ceramic capacitor

## Slide 6: Add heatshrink tubing

## Slide 7: Heatshrink tubing has little effect
Measured Q= 230

## Slide 8: Capacitive hat added using 34.5 inch lengths of enamel wire

## Slide 9: Measured Q=267 with capacitive hat

## Slide 10: With capacitive hat, the coil is well behaved to 20 MHz SRF is still about 40 MHz

## Slide 11: Conclusions
Q of loading coil used in XM-240 is around 250
The capacitive hat does not appear to affect coil performance at 7 MHz
Heatshrink has no effect on performance
NEC simulations by others indicate that a maximum gain of 0.5 db can be achieved by replacing these coils with airwound inductors having Q’s near 900